## Slide 1: Bringing the Analog World to Digital Design
Team Members:
Conor Naughton
Bin Xu
Yimin Xu

## Slide 2
Goals
Explore the use of analog signals
Deep dive into how Analog to Digital Converters (ADCs) work
Motivation
FPGAs work with digital signals however the tasks they are used for often involves analog inputs
Requires interacting with and controlling another component of the development board

## Slide 3: Game Description
Two player Pong
  Player 1: Paddle on right edge of screen controlled via board buttons
    Moves a discrete amount with each button press
      Demonstrates digital input
  Player 2: Paddle on bottom edge of screen controlled via analog controller
    Moves a variable amount based on analog controller value
      Demonstrates analog input
Gameplay
  Ball starts moving slowly in random direction
  Players move paddles to prevent ball from hitting the edge of the screen
  Score increases every time the ball hits the paddle
  Ball also moves faster each time it hits a paddle
  After achieving a certain score, a second ball is inserted into the game
  Once the ball does hit the edge of the screen, a “game over” screen appears
  After game is lost, user can display the configuration of paddles and ball when they lost by flipping a switch

## Slide 4: Analog to Digital Converter (ADC)
What is an ADC?
  HW that takes in an analog signal and converts it to a digital output
  In other words, it changes an analog signal that is continuous in terms of both time and amplitude to a digital signal that is discrete in terms of both time and amplitude
How does an ADC work?
  Analog input is sampled at a certain frequency
  Sample is quantized into a digital value by comparing with a reference voltage
  12-bit ADC => 4096 quantization levels
How does ADC sampling work?
  Choose sample rate so the digital output accurately reflects the input (≥ 2x the fastest input frequency)
  Max sample rate 1MSPS
Illustration of quantization levels
Illustration of analog input being approximated by a digital output

## Slide 5: Further ADC Details
What are the peripheral components to the ADC?
  Input mux
  Status and control registers
  Reference generator
  Dynamic Reconfiguration Port (DRP) Interface
What parameters define how the ADC works?
  Sample averaging
  Unipolar or differential measurement mode
  Settling time
Nexys A7 ADC Block Diagram
ADC Input/Output Signals
ADC Timing Diagram

## Slide 6: Force Sensitive Resistor (FSR)
FSR is an electrical component which changes its resistance when a force or pressure is applied.
Composed of two substrate layers sandwiching together a conductive film and a spacer.
The substrate layer on the spacer side also has a conductive ink printed on it.
More force => air pushed out of space => film contacts conductive print => resistance decreases
Problem: Not very differentiable (i.e., basically a 1 or 0)
Solution: Wheatstone Bridge
Wheatstone Bridge with a variable resistor Rx
Breakdown of Force Sensitive Resistor

## Slide 7: Pong Game
How did we change the game?
  We need to pass the analog signal to the game.
  Replaced the original input buttons with with the analog signal from the ADC.
  Added replay button for capturing the last image before game over.
  Capturing the end game signal to VGA.
  Getting the speed signal from ADC to control the speed of paddle movement.
How do we use the output of the ADC
  There is only one analog output each time. The signal is passed to the Analog2Game. Analog2Game will pass the direction to the game.

## Slide 8: VGA Controller
We also need to replay the last frame of game
Capture the position of paddle and square, send it to the VGA
Using mode switch to show the image we capture from the game

## Slide 9: Memory
What were we planning on doing with the memory?
  Record the process of playing and replay it after game over
Why didn’t it work?
  Possible overwritten data
  The delay of redrawing is overlapped by next redrawing
How does Quad SPI flash work?
  Not suitable for saving data
What did we end up doing instead?
  Saving images of game process such as when square hits the edge

## Slide 10: Block Diagram

## Slide 11: Verilog Example
ADC instantiation
  Initializing the control registers to define the ADC operation after configuration
  Connect ADC I/Os to the design
DRP is the interface between the ADC and FPGA through which the FPGA can access the ADC registers

## Slide 12: Demo Video
https://www.youtube.com/watch?v=pn7tEva09VU

## Slide 13: Successes
Got the game to work [Bin]
  Ball movement, start and end game display
Demonstrated analog nature of input sensor [Conor]
  Pressing harder makes it move faster
  Achieved using Wheatstone bridge setup
Multi-Channel ADC sampling [Conor]
Replaying final frame from game [Bin/Yimin]

## Slide 14: Failures
Use of Quad SPI flash memory
  Original plan was to demonstrate NVRAM
  Unable to figure out SPI protocol to interact with Quad SPI flash
ADC timing issue
  Despite flags, still had some issues with output from button press being applied to opposite

## Slide 15: GitHub Link
https://github.com/xu842251462/EC551_Final_Project

## Slide 16: References
https://github.com/Digilent/Nexys-A7-100T-XADC
https://github.com/chmo2019/EC311_Final_Project
https://www.chipverify.com/verilog/verilog-single-port-ram